## Slide 1: Spectrophotometry
meter means…
…measure,
-photo means…
…light, and
-spectro means…
…range.
Put them together, and we have a technique for analyzing samples based on the amount and colors of light that they absorb.

## Slide 2: Inside a Spectrophotometer…
Light Source
Diffraction Grating
Slit
Shutter
Sample
Cuvette
Photomultiplier Tube (PMT) Detector
Meter
% Transmittance
Absorbance
100
0
∞
0

## Slide 3: Spectrophotometry… spectral curves
If we measure the absorbance of a sample at many wavelengths, we can establish a spectral curve.
Every colored substance will absorb ONE color of light better than any other, creating a peak on the spectral curve. This peak will occur at the same wavelength every time that substance is present in a sample
If the spectral curve has more than one peak, it must contain more than one colored substance.
If the curve has only one peak, that does not necessarily mean that the sample is a pure substance, but it DOES mean that there is only one COLORED substance in the sample

## Slide 4: Spectrophotometry… spectral curves
3 things we know about a sample from its spectral curve.
Number of Peaks = Number of Colored components
Location (wavelength) of peak tells us the color of that component. (The color we see is the OPPOSITE of the color of light absorbed.)
Peak height (absorbance) is related to how much of the component is present.

## Slide 5: The Visible Spectrum…
…includes what colors?
red, orange, yellow, green, blue, violet
…corresponds to what wavelengths?
400 nm to 700 nm
How can we tell the color of light by the wavelength?
400
450
500
600
650
700
550

## Slide 6: What Kool-Aid Flavor is this?
Chart: Wavelength (nm)
| 400 | 425 | 450 | 475 | 500 | 525 | 550 | 575 | 600 | 625 | 650 | 675 | 700
Cherry | 0.44 | 0.52 | 0.71 | 1.12 | 1.45 | 1.25 | 0.76 | 0.24 | 0.094 | 0.07 | 0.095 | 0.111 | 0.151
Cherry!

## Slide 7: What Kool-Aid Flavor is this?
Chart: Wavelength (nm)
| 400 | 425 | 450 | 475 | 500 | 525 | 550 | 575 | 600 | 625 | 650 | 675 | 700
Grape | 0.18 | 0.16 | 0.186 | 0.302 | 0.36 | 0.349 | 0.27 | 0.199 | 0.259 | 0.39 | 0.316 | 0.126 | 0.11
Grape!

## Slide 8: What Kool-Aid Flavor is this?
Chart: Wavelength (nm)
| 400 | 425 | 450 | 475 | 500 | 525 | 550 | 575 | 600 | 625 | 650 | 675 | 700
Lemon-Lime | 0.223 | 0.295 | 0.231 | 0.153 | 0.068 | 0.049 | 0.039 | 0.042 | 0.074 | 0.105 | 0.093 | 0.072 | 0.078
Lemon-Lime!

## Slide 9: Spectrophotometry
lmax is the wavelength of maximum absorbance.
This will occur at a wavelength within the color range of the opposite color of the sample.
The Beer-Lambert Law says that the absorbance of a sample at lmax is proportional to the concentration of the color absorbing species in the sample.

## Slide 10: Spectrophotometry
PROPER HANDLING OF CUVETTES
Do not use abrasive materials to clean cuvettes.
Once a cuvette has been cleaned, take care NOT to touch the but (bottom half) of the cuvette. (Don’t be like Nemo!)
If you get fingerprints on cuvettes, wipe them off with a TISSUE NOT A PAPER TOWEL
When finished with the lab, STILL DON”T TOUCH THE BUT! Dump the contents of the cuvettes down the drain and give them a quick rinse with distilled water.